## Slide 1: Outline
The Design Procedure
Moore Sequence Detector
Mealy Sequence Detector
Tracing State Diagrams and Verifying Correctness
Sequential Comparator
Binary Counter
Up/Down Counter with Enable

## Slide 2: The Design Procedure
Given a Description (or Specification) of the Problem
Obtain a state diagram for the sequential circuit
Assign binary codes to the states and fill the state table
Select the type of Flip-Flops and derive the FF input equations
Derive the output equations
Draw the circuit diagram
Verify the correctness of the final design (verification)

## Slide 3: The State Diagram
A state is an abstraction of memory
A state remembers a history of inputs applied to the circuit
Examples:
  State S0 represents the fact that the last input is a 0
  State S1 represents the fact that the last input is a 1
  State S2 represents the fact that the last two-input sequence is "11"
Obtaining the state diagram is the most important step
Requires experience and good understanding of the problem

## Slide 4: Example: Sequence Detector
A sequence detector is a sequential circuit
Detects a specific sequence of bits in the input
The input is a serial bit stream:
One input bit is fed to the sequence detector each cycle
The output is also a bit stream: One output bit each cycle
Indicates whether a given sequence is detected or not
Sequence Detector

## Slide 5: State Diagram for a Sequence Detector
S3
1
S2
1
S1
1
Example: Design a circuit that detects the input sequence "111"
Begin in an initial state: call it S0
S0 indicates that a 1 is NOT detected yet
As long as the input is 0, remain in the initial state S0
Add a state (call it S1) that detects the first 1 in the input
Add a state (call it S2) that detects the input sequence "11"
Add a state (call it S3) that detects the input sequence "111"
S0
0

## Slide 6: Complete the State Diagram
0
Moore Design: Assign Output to States
The output in S0, S1, and S2 should be 0
The output in S3 should be 1
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Now complete the state diagram:
Add transitions from S1, S2, S3 back to S0 if the input is 0
Add transition from S3 to itself if the input is 1 to detect sequences longer than three 1's

## Slide 7: State Assignment
Each state must be assigned a unique binary code
If there are states then
The minimum number of state bits:
is the smallest integer ≥ (ceiling function)
In our example, there are four states: S0, S1, S2, and S3
Therefore, the minimum number of state bits (Flip-Flops) = 2
State assignment: S0 = 00, S1 = 01, S2 = 10 and S3 = 11
If bits are used, the number of unused states =
In our example, there are NO unused states

## Slide 8: From State Diagram to State Table
0
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Present State | Next State |  | Output
 | = 0 | = 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S0 | S3 | 0
S3 | S0 | S3 | 1
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
State Assignment
S0 = 00, S1 = 01
S2 = 10, S3 = 11

## Slide 9: Structure of a Moore Sequence Detector
In our design examples, only D-type Flip-Flops will be used
They are the simplest to analyze and implement
Next, we need minimal expressions for
Next State Logic
Output Logic
Next State
Logic
D Flip
Flops
Next
State
Current
State
Output
Logic
clock

## Slide 10: Derive Next State an Output Equations
Two D-type Flips-Flops
Present State = Flip-Flop Outputs and
Next State = Flip-Flop Inputs and
Next State equations: and
Output equation: (from the state diagram)
Present State | Next State |  | Output
 | = 0 | = 1 | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
Present State | Next State |  | 
0 0 | 0 0 | 0 1 | 0
0 1 | 0 0 | 1 0 | 0
1 0 | 0 0 | 1 1 | 0
1 1 | 0 0 | 1 1 | 1
0
1
00
01
11
10
0
0
0
1
0
1
0
1
0
1
00
01
11
10
0
1
0
0
0
1
0
1

## Slide 11: Draw the Moore Sequence Detector Circuit
Output
Logic
Next State Logic
,

## Slide 12: Mealy Type Sequence Detector
Let us redesign a Mealy type "111" sequence detector
The initial state S0 indicates that a 1 is NOT detected yet
As long as the input is 0, remain in the initial state S0
Notice that input / output is written on the arc (Mealy type)
Add a state (call it S1) that detects the first 1 in the input
Add a state (call it S2) that detects the input sequence "11"
S0
0 / 0
1 / 0
S1
1 / 0
S2

## Slide 13: Complete the Mealy State Diagram
0 / 0
0 / 0
State S2 is reached after detecting the input sequence "11"
At S2, if the next input is 1 then the output should be 1
Make a transition from S2 back to itself labeled 1 / 1
No need for state S3, because output is on the arc
Now complete the state diagram
Add transitions from S1 and S2 back to S0 when input is 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
Mealy Machines typically use
less states than Moore Machines

## Slide 14: State Assignment and State Table
Three States  Minimum number of state bits (Flip-Flops) = 2
Assign: S0 = 00, S1 = 01, and S2 = 10 (State 11 is Unused)
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  |  | 
S0 | S0 | S1 | 0 | 0
S1 | S0 | S2 | 0 | 0
S2 | S0 | S2 | 0 | 1
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1

## Slide 15: Derive Next State and Output Equations
Present State = Flip-Flop Outputs and (state 11 is unused)
Next State = Flip-Flop Inputs and
Flip-Flop Input equations: and
Output equation:
Present State | Next State |  | Output | 
 | = 0 | = 1 | = 0 | = 1
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
Present State | Next State |  |  | 
0 0 | 0 0 | 0 1 | 0 | 0
0 1 | 0 0 | 1 0 | 0 | 0
1 0 | 0 0 | 1 0 | 0 | 1
1 1 | X X | X X | X | X
0
1
00
01
11
10
0
0
0
1
X
X
0
1
0
1
00
01
11
10
0
1
0
0
X
X
0
0
0
1
00
01
11
10
0
0
0
0
X
X
0
1

## Slide 16: Draw the Mealy Sequence Detector Circuit
Reset
Output Logic
Next State
Logic
Next State
Logic

## Slide 17: Mealy versus Moore Sequence Detector
In general, Moore state diagrams have more states than corresponding Mealy.
The drawback of Mealy is that glitches can appear in the output if the input is not synchronized with the clock.
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
1 / 0
S2
1 / 1
0
0
0
S0
0
S1
0
S2
0
S3
1
1
1
1
0
1
Mealy Sequence Detector
Moore
Sequence
Detector

## Slide 18: Verification
Sequential circuits should be verified by showing that the circuit produces the original state diagram
Verification can be done manually, or with the help of a simulation program
All possible input combinations are applied at each state and the state variables and outputs are observed
A reset input is used to reset the circuit to its initial state
Apply a sequence of inputs to test all the state-input combinations, i.e., all transitions in the state diagram
Observe the output and the next state that appears after each clock edge in the timing diagram

## Slide 19: Input Test Sequence
Required to verify the correct operation of a sequential circuit
It should test each state transition of the state diagram
Test sequences can be produced from the state diagram
Consider the Mealy sequence detector, starting at S0 (reset), we can use an input test sequence to verify all state transitions:
Input test sequence: reset then x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
reset
1 / 0
S2
1 / 1
Reset input forces initial state to be S0

## Slide 20: Verifying the Mealy Sequence Detector
Q0
Q1
S0
S0
S1
S0
S1
S2
S0
S1
S2
S2
Input test sequence: reset then x = 0, 1, 0, 1, 1, 0, 1, 1, 1, 1
0 / 0
0 / 0
S0
0 / 0
1 / 0
S1
reset
1 / 0
S2
1 / 1
z
reset
x
0
1
0
1
1
0
1
1
1
1
clock
cc0
cc1
cc2
cc3
cc4
cc5
cc6
cc7
cc8
cc9
cc10
0
0
0
0
0
0
0
0
1
1
glitch

## Slide 21: Sequential Comparator
Problem Description:
Design a sequential circuit that compares two numbers A and B
Two Inputs: A and B
A consists of n bits
B consists of n bits
Bit streaming starting at bit 0
Compare A0 with B0, A1 with B1, etc. (Bit 0 is least significant bit)
A reset signal resets the comparator to its initial state
Reset is required before starting a new comparison
Two outputs: GT (Greater Than) and LT (Less Than)
Sequential
Comparator

## Slide 22: Designing the State Diagram
01
10
00, 11, 10
00, 11, 01
GT
10
10
01
LT
01
Reset: start initially in state EQ
EQ indicates Equality (output is 00)
Stay in EQ as long as AiBi = 00 or 11
Go to LT if Ai < Bi (AiBi = 01)
LT indicates Less Than (output is 01)
Go to GT if Ai > Bi (AiBi = 10)
GT is Greater Than (output is 10)
Complete the state diagram
LT  GT and GT  LT
LT  LT and GT  GT
EQ
00
Reset
00, 11
Moore State Diagram

## Slide 23: State Assignment and State Table
Three States  Two Flip-Flops
D-type Flip-Flops will be used
State Assignment: EQ = 00, LT = 01, GT = 10
Output = Present State (Q1 and Q0)
01
10
00, 11, 10
00, 11, 01
GT
10
10
01
LT
01
EQ
00
Reset
00, 11
Present State Q1 Q0 | Next State (D1 D0) |  |  | 
 | A B 0 0 | A B 0 1 | A B 1 0 | A B 1 1
0 0 | 0 0 | 0 1 | 1 0 | 0 0
0 1 | 0 1 | 0 1 | 1 0 | 0 1
1 0 | 1 0 | 0 1 | 1 0 | 1 0
1 1 | X X | X X | X X | X X

## Slide 24: Deriving the Next State Equations
State 11 is unused
When present state is 11, don't cares are used to fill the next state.
Output = Present state
00
01
11
10
00
01
11
10
1
X
0
0
0
X
0
0
1
X
0
0
1
X
1
1
00
01
11
10
00
01
11
10
0
X
0
1
1
X
1
1
0
X
0
1
0
X
0
0
Present State Q1 Q0 | Next State (D1 D0) |  |  | 
 | A B 0 0 | A B 0 1 | A B 1 0 | A B 1 1
0 0 | 0 0 | 0 1 | 1 0 | 0 0
0 1 | 0 1 | 0 1 | 1 0 | 0 1
1 0 | 1 0 | 0 1 | 1 0 | 1 0
1 1 | X X | X X | X X | X X

## Slide 25: Sequential Comparator Circuit Diagram

## Slide 26: Designing with Unused States
A circuit with n flip-flops has 2n binary states
However, the state diagram may have m states
Therefore, the number of unused states = 2n – m
Unused states do not appear in the state diagram
  Sometimes treated as don't cares when simplifying expressions in K-maps
However, it is possible to enter an unused state!
  Caused by outside interference or a circuit malfunction
Must specify the output and next state values for unused states
A special (invalid) output can be used to indicate an unused state
A return to a valid state must be possible without reset
  Next state for unused states should be specified (NOT don't cares!)

## Slide 27: Design of a Binary Counter
Problem Specification:
Design a circuit that counts up from 0 to 7 then back to 0
000  001  010  011  100  101  110  111  000
When reaching 7, the counter goes back to 0 then goes up again
There is no input to the circuit
The counter is incremented each cycle
The output of the circuit is the present state (count value)
The circuit should be designed using D-type Flip-Flops

## Slide 28: Designing the State Diagram
Eight states are needed to store the count values 0 to 7
No input, state transition happens at the edge of each cycle
S0
S4
S2
S6
S1
S7
S5
S3
Each state is
assigned a unique
binary count value
Three Flip-Flops
are required for
the eight states

## Slide 29: State Table
Only two columns: Present State and Next State
State changes each cycle
000
100
010
110
001
111
101
011
Present State Q2 Q1 Q0 | Next State D2 D1 D0
0 0 0 | 0 0 1
0 0 1 | 0 1 0
0 1 0 | 0 1 1
0 1 1 | 1 0 0
1 0 0 | 1 0 1
1 0 1 | 1 1 0
1 1 0 | 1 1 1
1 1 1 | 0 0 0

## Slide 30: Deriving the Next State Equations
⨁
0
1
00
01
11
10
0
0
0
1
1
0
1
1
Present State Q2 Q1 Q0 | Next State D2 D1 D0
0 0 0 | 0 0 1
0 0 1 | 0 1 0
0 1 0 | 0 1 1
0 1 1 | 1 0 0
1 0 0 | 1 0 1
1 0 1 | 1 1 0
1 1 0 | 1 1 1
1 1 1 | 0 0 0
0
1
00
01
11
10
0
1
1
0
1
0
0
1
0
1
00
01
11
10
1
0
1
0
1
0
1
0

## Slide 31: 3-Bit Counter Circuit Diagram
⨁
Output = 3-bit Count Value

## Slide 32: Up/Down Counter with Enable
Problem Specification:
Design a 2-bit Up / Down counter
Two inputs: E (Enable) and U (Up)
If E = 0 then counter remains in the same state (regardless of U)
If EU = 11 then count up from 0 to 3, then back to 0
If EU = 10 then count down from 3 down to 0, then back to 3
The output of the counter is the present state (count value)
The circuit should be designed using T Flip-Flops
A reset signal resets the counter to its initial state

## Slide 33: Designing the State Diagram
Four states are required
to store the count 0 to 3
Count up if EU = 11
Count down if EU = 10
Disable counter if E = 0
Transition to same state if
EU = 00 or 01
Asynchronous reset to
start initially at state S0
E = 0
E = 0
E = 0
E = 0
EU = 11
EU = 11
EU = 11
EU = 11
EU = 10
EU = 10
EU = 10
EU = 10
S0
S1
S3
S2
Reset

## Slide 34: State Assignment and State Table
Four States  Two State variables (2 Flip-Flops)
State Assignment: S0 = 00, S1 = 01, S2 = 10, and S3 = 11
Present State Q1 Q0 | Next State |  |  | 
 | E U 0 0 | E U 0 1 | E U 1 0 | E U 1 1
0 0 | 0 0 | 0 0 | 1 1 | 0 1
0 1 | 0 1 | 0 1 | 0 0 | 1 0
1 0 | 1 0 | 1 0 | 0 1 | 1 1
1 1 | 1 1 | 1 1 | 1 0 | 0 0
E = 0
E = 0
E = 0
E = 0
EU = 11
EU = 11
EU = 11
EU = 11
EU = 10
EU = 10
EU = 10
EU = 10
00
01
11
10
Reset

## Slide 35: Excitation Table for Flip-Flops
Excitation Table:
Lists the required input for next state transition
For D Flip-Flop: Input = Next State
For T Flip-Flop: Input
Excitation tables are used to find the Flip-Flop input equations
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Excitation Tables for the D and T Flip-Flops

## Slide 36: Deriving the T-Flip-Flop Input Equations
Present State Q1 Q0 | Next State at (t+1) |  |  | 
 | E U 0 0 | E U 0 1 | E U 1 0 | E U 1 1
0 0 | 0 0 | 0 0 | 1 1 | 0 1
0 1 | 0 1 | 0 1 | 0 0 | 1 0
1 0 | 0 | 1 0 | 0 1 | 1 1
1 1 | 1 | 1 1 | 1 0 | 0 0
Present State Q1 Q0 | Flip-Flop Inputs T1 T0 |  |  | 
 | E U 0 0 | E U 0 1 | E U 1 0 | E U 1 1
0 0 | 0 0 | 0 0 | 1 1 | 0 1
0 1 | 0 0 | 0 0 | 0 1 | 1 1
1 0 | 0 0 | 0 0 | 1 1 | 0 1
1 1 | 0 0 | 0 0 | 0 1 | 1 1
00
01
11
10
00
01
11
10
0
0
0
0
0
0
0
0
0
1
0
1
1
0
1
0
00
01
11
10
00
01
11
10
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1

## Slide 37: 2-bit Up/Down Counter Circuit Diagram
2-bit Count Value