## Slide 1: Boolean Algebra and Logic Gates
Digital Logic Design

## Slide 2: Presentation Outline
Boolean Algebra
Boolean Functions and Truth Tables
DeMorgan's Theorem
Algebraic manipulation and expression simplification
Logic gates and logic diagrams
Minterms and Maxterms
Sum-Of-Products and Product-Of-Sums

## Slide 3: Boolean Algebra
Introduced by George Boole in 1854
Two-valued Boolean algebra is also called switching algebra
A set of two values: B = {0, 1}
Three basic operations: AND, OR, and NOT
The AND operator is denoted by a dot (·)
  or is read: AND
The OR operator is denoted by a plus (+)
  is read: OR
The NOT operator is denoted by (') or an overbar (¯).
  or is the complement of

## Slide 4: Postulates of Boolean Algebra
1. Closure: the result of any Boolean operation is in B = {0, 1}
2. Identity element with respect to + is 0:
Identity element with respect to · is 1:
3. Commutative with respect to +:
Commutative with respect to ·:
4. · is distributive over +:
+ is distributive over ·:
5. For every in B, there exists in B (called complement of ) such that: and

## Slide 5: AND, OR, and NOT Operators
The following tables define , , and
is the AND operator
is the OR operator
is the NOT operator
x y | x·y
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
x y | x+y
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 1
x | x'
0 | 1
1 | 0

## Slide 6: Boolean Functions
Boolean functions are described by expressions that consist of:
  Boolean variables, such as: , , etc.
  Boolean constants: 0 and 1
  Boolean operators: AND (·), OR (+), NOT (')
  Parentheses, which can be nested
Example:
  The dot operator is implicit and need not be written
Operator precedence: to avoid ambiguity in expressions
  Expressions within parentheses should be evaluated first
  The NOT (') operator should be evaluated second
  The AND (·) operator should be evaluated third
  The OR (+) operator should be evaluated last

## Slide 7: Truth Table
A truth table can represent a Boolean function
List all possible combinations of 0's and 1's assigned to variables
If n variables then 2n rows
Example: Truth table for
x y z | y' | xy' | x' | x'z | f = xy'+ x'z
0 0 0 | 1 | 0 | 1 | 0 | 0
0 0 1 | 1 | 0 | 1 | 1 | 1
0 1 0 | 0 | 0 | 1 | 0 | 0
0 1 1 | 0 | 0 | 1 | 1 | 1
1 0 0 | 1 | 1 | 0 | 0 | 1
1 0 1 | 1 | 1 | 0 | 0 | 1
1 1 0 | 0 | 0 | 0 | 0 | 0
1 1 1 | 0 | 0 | 0 | 0 | 0

## Slide 8: DeMorgan's Theorem
x | y | x' | y' | x+y | (x+y)' | x'y' | x y | (x y)' | x'+ y'
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
Can be verified
Using a Truth Table
Identical
Identical
Generalized DeMorgan's Theorem:

## Slide 9: Complementing Boolean Functions
What is the complement of ?
Use DeMorgan's Theorem:
  Complement each variable and constant
  Interchange AND and OR operators
So, what is the complement of ?
Answer: )
Example 2: Complement
Answer:

## Slide 10: Algebraic Manipulation of Expressions
The objective is to acquire skills in manipulating Boolean expressions, to transform them into simpler form.
Example 1: prove (absorption theorem)
Proof:
Distributive · over +
Example 2: prove (simplification theorem)
Proof: Distributive + over ·

## Slide 11: Consensus Theorem
Prove that: (consensus theorem)
Proof:
Distributive · over +
Associative commutative +
Distributive · over +

## Slide 12: Summary of Boolean Algebra
 | Property | Dual Property
Identity |  | 
Complement |  | 
Null |  | 
Idempotence |  | 
Involution | ( | 
Commutative |  | 
Associative | ( | 
Distributive |  | 
Absorption |  | 
Simplification |  | 
De Morgan | ( | 
 | Property | Dual Property
Identity |  | 
Complement |  | 
Null |  | 
Idempotence |  | 
Involution |  | 
Commutative |  | 
Associative |  | 
Distributive |  | 
Absorption |  | 
Simplification |  | 
De Morgan |  | 

## Slide 13: Duality Principle
The dual of a Boolean expression can be obtained by:
  Interchanging AND (·) and OR (+) operators
  Interchanging 0's and 1's
Example: the dual of is
  The complement operator does not change
The properties of Boolean algebra appear in dual pairs
  If a property is proven to be true then its dual is also true
 | Property | Dual Property
Identity |  | 
Complement |  | 
Distributive |  | 
 | Property | Dual Property
Identity |  | 
Complement |  | 
Distributive |  | 

## Slide 14: Expression Simplification
Using Boolean algebra to simplify expressions
Expression should contain the smallest number of literals
A literal is a variable that may or may not be complemented
Example: simplify
Solution: (15 literals)
(15 literals)
(13 literals)
(7 literals)
(7 literals)
(6 literals)
(5 literals only)

## Slide 15: Importance of Boolean Algebra
Our objective is to learn how to design digital circuits
These circuits use signals with two possible values
Logic 0 is a low voltage signal (around 0 volts)
Logic 1 is a high voltage signal (e.g. 5 or 3.3 volts)
The physical value of a signal is the actual voltage it carries, while its logic value is either 0 (low) or 1 (high)
Having only two logic values (0 and 1) simplifies the implementation of the digital circuit

## Slide 16: Next . . .
Boolean Algebra
Boolean Functions and Truth Tables
DeMorgan's Theorem
Algebraic manipulation and expression simplification
Logic gates and logic diagrams
Minterms and Maxterms
Sum-Of-Products and Product-Of-Sums

## Slide 17: Logic Gates and Symbols
AND gate
OR gate
NOT gate (inverter)
In the earliest computers, relays were used as mechanical switches controlled by electricity (coils)
Today, tiny transistors are used as electronic switches that implement the logic gates (CMOS technology)
AND: Switches in series
logic 0 is open switch
OR: Switches in parallel
logic 0 is open switch
NOT: Switch is normally
closed when x is 0

## Slide 18: Truth Table and Logic Diagram
Given the following logic function:
Draw the corresponding truth table and logic diagram
Truth Table
x y z | y'+ z | f = x(y'+ z)
0 0 0 | 1 | 0
0 0 1 | 1 | 0
0 1 0 | 0 | 0
0 1 1 | 1 | 0
1 0 0 | 1 | 1
1 0 1 | 1 | 1
1 1 0 | 0 | 0
1 1 1 | 1 | 1
Truth Table and Logic Diagram describe the same function .
Truth table is unique, but logic expression and logic diagram are not. This gives flexibility in implementing logic functions.
Logic Diagram

## Slide 19: Combinational Circuit
A combinational circuit is a block of logic gates having:
inputs:
outputs:
Each output is a function of the input variables
Each output is determined from present combination of inputs
Combination circuit performs operation specified by logic gates

Combinational
Circuit

inputs
outputs

## Slide 20: Example of a Simple Combinational Circuit
The above circuit has:
  Three inputs: , , and
  Two outputs: and
What are the logic expressions of and ?
Answer:

## Slide 21: From Truth Tables to Gate Implementation
Given the truth table of a Boolean function , how do we implement the truth table using logic gates?
Truth Table
x y z | f
0 0 0 | 0
0 0 1 | 0
0 1 0 | 1
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 0
1 1 1 | 1
What is the logic expression of ?
What is the gate implementation of ?
To answer these questions, we need to define Minterms and Maxterms

## Slide 22: Minterms and Maxterms
Minterms are AND terms with every variable present in either true or complement form
Maxterms are OR terms with every variable present in either true or complement form
Minterms and Maxterms for 2 variables and
For n variables, there are 2n Minterms and Maxterms
x | y | index | Minterm | Maxterm
0 | 0 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 2 |  | 
1 | 1 | 3 |  | 
x | y | index | Minterm | Maxterm
0 | 0 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 2 |  | 
1 | 1 | 3 |  | 

## Slide 23: Minterms and Maxterms for 3 Variables
Maxterm is the complement of Minterm
and
x | y | z | index | Minterm | Maxterm
0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 2 |  | 
0 | 1 | 1 | 3 |  | 
1 | 0 | 0 | 4 |  | 
1 | 0 | 1 | 5 |  | 
1 | 1 | 0 | 6 |  | 
1 | 1 | 1 | 7 |  | 
x | y | z | index | Minterm | Maxterm
0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 2 |  | 
0 | 1 | 1 | 3 |  | 
1 | 0 | 0 | 4 |  | 
1 | 0 | 1 | 5 |  | 
1 | 1 | 0 | 6 |  | 
1 | 1 | 1 | 7 |  | 

## Slide 24: Purpose of the Index
Minterms and Maxterms are designated with an index
The index for the Minterm or Maxterm, expressed as a binary number, is used to determine whether the variable is shown in the true or complemented form
For Minterms:
  ‘1’ means the variable is Not Complemented
  ‘0’ means the variable is Complemented
For Maxterms:
  ‘0’ means the variable is Not Complemented
  ‘1’ means the variable is Complemented

## Slide 25: Sum-Of-Minterms (SOM) Canonical Form
Sum of Minterm entries that evaluate to ‘1’
Truth Table
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
Focus on the ‘1’ entries

## Slide 26: Examples of Sum-Of-Minterms

## Slide 27: Product-Of-Maxterms (POM) Canonical Form
Truth Table
x y z | f | Maxterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
x y z | f | Maxterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
Product of Maxterm entries that evaluate to ‘0’
Focus on the ‘0’ entries

## Slide 28: Examples of Product-Of-Maxterms

## Slide 29: Conversions between Canonical Forms
The same Boolean function can be expressed in two ways:
  Sum-of-Minterms
  Product-of-Maxterms
x y z | f | Minterms | Maxterms
0 0 0 | 1 |  | 
0 0 1 | 0 |  | 
0 1 0 | 1 |  | 
0 1 1 | 1 |  | 
1 0 0 | 0 |  | 
1 0 1 | 1 |  | 
1 1 0 | 0 |  | 
1 1 1 | 1 |  | 
x y z | f | Minterms | Maxterms
0 0 0 | 1 |  | 
0 0 1 | 0 |  | 
0 1 0 | 1 |  | 
0 1 1 | 1 |  | 
1 0 0 | 0 |  | 
1 0 1 | 1 |  | 
1 1 0 | 0 |  | 
1 1 1 | 1 |  | 
To convert from one canonical form to another, interchange the symbols  and  and list those numbers missing from the original form.
Truth Table

## Slide 30: Function Complement
Given a Boolean function
Then, the complement of function
x y z | f | f'
0 0 0 | 1 | 0
0 0 1 | 0 | 1
0 1 0 | 1 | 0
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 0 | 1
1 1 1 | 1 | 0
The complement of a function expressed by a Sum of Minterms is the Product of Maxterms with the same indices. Interchange the symbols  and , but keep the same list of indices.
Truth Table

## Slide 31: Summary of Minterms and Maxterms
There are 2n Minterms and Maxterms for Boolean functions with n variables, indexed from 0 to 2n – 1
Minterms correspond to the 1-entries of the function
Maxterms correspond to the 0-entries of the function
Any Boolean function can be expressed as a Sum-of-Minterms and as a Product-of-Maxterms
For a Boolean function, given the list of Minterm indices one can determine the list of Maxterms indices (and vice versa)
The complement of a Sum-of-Minterms is a Product-of-Maxterms with the same indices (and vice versa)

## Slide 32: Sum-of-Products and Products-of-Sums
Canonical forms contain a larger number of literals
  Because the Minterms (and Maxterms) must contain, by definition, all the variables either complemented or not
Another way to express Boolean functions is in standard form
Two standard forms: Sum-of-Products and Product-of -Sums
Sum of Products (SOP)
  Boolean expression is the ORing (sum) of AND terms (products)
  Examples:
Products of Sums (POS)
  Boolean expression is the ANDing (product) of OR terms (sums)
  Examples:

## Slide 33: Two-Level Gate Implementation
3-input AND gate
AND-OR
implementations
3-input OR gate
OR-AND
implementations

## Slide 34: Two-Level vs. Three-Level Implementation
(6 literals) is a sum-of-products
may also be written as: (5 literals)
However, is a non-standard form
  is not a sum-of-products nor a product-of-sums
2-level implementation
3-level implementation
3-input OR gate