## Slide 1: Sequential Circuits
Digital Logic Design

## Slide 2: Outline
Introduction to Sequential Circuits
Synchronous versus Asynchronous
Latches
Flip-Flops
Characteristic Tables and Equations

## Slide 3: Combinational versus Sequential
Two classes of digital circuits
  Combinational Circuits
  Sequential Circuits
Combinational Circuit
  Outputs = F(Inputs)
  Function of Inputs only
  NO internal memory
Sequential Circuit
  Outputs is a function of Inputs and internal Memory
  There is an internal memory that stores the state of the circuit
  Time is very important: memory changes with time
Combinational
Circuit
Inputs
Outputs

## Slide 4: Introduction to Sequential Circuits
A Sequential circuit consists of:
Memory elements:
  Latches or Flip-Flops
  Store the Present State
Combinational Logic
  Computes the Outputs of the circuit
  Outputs depend on Inputs and Current State
  Computes the Next State of the circuit
  Next State also depends on the Inputs and the Present State
Combinational
Logic
Memory
Elements
Inputs
Outputs
Next
State
Present
State

## Slide 5: Two Types of Sequential Circuits
Synchronous Sequential Circuit
  Uses a clock signal as an additional input
  Changes in the memory elements are controlled by the clock
  Changes happen at discrete instances of time
Asynchronous Sequential Circuit
  No clock signal
  Changes in the memory elements can happen at any instance of time
Our focus will be on Synchronous Sequential Circuits
  Easier to design and analyze than asynchronous sequential circuits

## Slide 6: Synchronous Sequential Circuits
Synchronous sequential circuits use a clock signal
The clock signal is an input to the memory elements
The clock determines when the memory should be updated
The present state = output value of memory (stored)
The next state = input value to memory (not stored yet)
Clock
Combinational
Logic
Memory
Elements
Inputs
Outputs
Next
State
Present
State

## Slide 7: The Clock
Clock is a periodic signal = Train of pulses (1's and 0's)
The same clock cycle repeats indefinitely over time
Positive Pulse: when the level of the clock is 1
Negative Pulse: when the level of the clock is 0
Rising Edge: when the clock goes from 0 to 1
Falling Edge: when the clock goes from 1 down to 0
Time
Clock cycle
Clock cycle
Positive
Pulse
Negative
Pulse

## Slide 8: Clock Cycle versus Clock Frequency
Clock cycle (or period) is a time duration
  Measured in seconds, milli-, micro-, nano-, or pico-seconds
  1 ms = 10-3 sec, 1 µs = 10-6 sec, 1 ns = 10-9 sec, 1 ps = 10-12 sec
Clock frequency = number of cycles per second (Hertz)
  1 Hz = 1 cycle/sec, 1 KHz = 103 Hz, 1 MHz = 106 Hz, 1 GHz = 109 Hz
Clock frequency = 1 / Clock Cycle
  Example: Given the clock cycle = 0.5 ns = 0.5 ×10-9 sec
  Then, the clock frequency = 1/(0.5×10-9) = 2×109 Hz = 2 GHz
Time
Clock cycle
Clock cycle
Clock cycle

## Slide 9: Memory Elements
Memory can store and maintain binary state (0's or 1's)
  Until directed by an input signal to change state
Main difference between memory elements
  Number of inputs they have
  How the inputs affect the binary state
Two main types:
  Latches are level-sensitive (the level of the clock)
  Flip-Flops are edge-sensitive (sensitive to the edge of the clock)
Flip-Flips are used in synchronous sequential circuits
Flip-Flops are built with latches

## Slide 10: SR Latch
A latch is binary storage element that can store 0 or 1
It is the most basic memory element
An SR Latch can be built using two NOR gates
Two inputs: (Set) and (Reset)
Two outputs: and

## Slide 11: SR Latch Operation
If and then Set ()
If and then Reset ()
When , and are unchanged
The latch stores its outputs and as long as
When , and are undefined (should never be used)

## Slide 12: S R Latch with NAND Gates
If and then Set ()
If and then Reset ()
When , and are unchanged (remain the same)
The latch stores its outputs and as long as
When , and are undefined (should never be used)
Known as
the Latch

## Slide 13: SR Latch with a Clock Input
An additional Clock input signal C is used
Clock controls when the state of the latch can be changed
When C=0, the S and R inputs have no effect on the latch
The latch will remain in the same state, regardless of S and R
When C=1, then normal SR latch operation
S
R

## Slide 14: D-Latch with a Clock Input
Only one data input
An inverter is added: and
and can never be 11 simultaneously  No undefined state
When , remains the same (No change in state)
When , and
S
R

## Slide 15: Graphic Symbols for Latches
A bubble appears at the complemented output
Indicates that is the complement of
A bubble also appears at the inputs of an latch
Indicates that logic-0 is used (not logic-1) to set (or reset) the latch (as in the NAND latch implementation)

## Slide 16: Problem with Latches
A latch is level-sensitive (sensitive to the level of the clock)
As long as the clock signal is high …
Any change in the value of input appears in the output
Output keeps changing its value during a clock cycle
Final value of output is uncertain
Due to this uncertainty, latches are NOT used as memory elements in synchronous circuits

## Slide 17: Flip-Flops
A Flip-Flop is a better memory element for synchronous circuits
Solves the problem of latches in synchronous sequential circuits
A latch is sensitive to the level of the clock
However, a flip-flop is sensitive to the edge of the clock
A flip-flop is called an edge-triggered memory element
It changes it output value at the edge of the clock
Time
Rising edge
Falling edge
Rising edge
Falling edge
High
Level
Low
Level

## Slide 18: Positive Edge-Triggered D Flip-Flop
Built using two latches in a master-slave configuration
A master latch (D-type) receives external inputs
A slave latch (SR-type) receives inputs from the master latch
Only one latch is enabled at any given time
  When C=0, the master is enabled and the D input is latched (slave disabled)
  When C=1, the slave is enabled to generate the outputs (master is disabled)
Outputs change when C changes from 0 to 1
Master
Slave

## Slide 19: Negative Edge-Triggered D Flip-Flop
Similar to positive edge-triggered flip-flop
The first inverter at the Master C input is removed
Only one latch is enabled at any given time
  When C=1, the master is enabled and the D input is latched (slave disabled)
  When C=0, the slave is enabled to generate the outputs (master is disabled)
Outputs change when C changes from 1 to 0
Master
Slave

## Slide 20: D Flip-Flop Timing Diagram
The diagram shows the timing of a positive edge D Flip-Flop
The rising edge of the clock triggers the D Flip-Flop
Initially, the value of q might be unknown
Notice the slight delay in the output q (after the rising edge)

## Slide 21: Graphic Symbols for Flip-Flops
A Flip-Flop has a similar symbol to a Latch
The difference is the arrowhead at the clock input C
The arrowhead indicates sensitivity to the edge of the clock
A bubble at the C input indicates negative edge-triggered FF
D Flip
Flop
D Flip
Flop

## Slide 22: D Flip-Flop with Asynchronous Reset
When Flip-Flops are powered, their initial state is unknown
Some flip-flops have an Asynchronous Reset input R
Resets the state (to logic value 0), independent of the clock
This is required to initialize a circuit before operation
If the R input is inverted (bubble) then R = 0 resets the flip-flop
D Flip
Flop
Inputs |  |  | Outputs | 
0 | X | X | 0 | 1
1 | 0 | ↑ | 0 | 1
1 | 1 | ↑ | 1 | 0
Inputs |  |  | Outputs | 
0 | X | X | 0 | 1
1 | 0 | ↑ | 0 | 1
1 | 1 | ↑ | 1 | 0
Function Table

## Slide 23: JK Flip-Flop
The D Flip-Flop is the most commonly used type
The JK is another type of Flip-Flop with inputs: J, K, and Clk
When JK = 10  Set, When JK = 01  Reset
When JK = 00  No change, When JK = 11  Invert outputs
JK can be implemented using two Clocked SR latches and gates
SR Latch
SR Latch
Master
Slave

## Slide 24: T Flip-Flop
The T (Toggle) flip-flop has inputs: T and Clk
When T = 0  No change, When T = 1  Invert outputs
The T flip-flop can be implemented using a JK flip-flop
It can also be implemented using a D flip-flop and a XOR gate

## Slide 25: Flip-Flop Characteristic Table
Defines the operation of a flip-flop in a tabular form
Next state is defined in terms of the current state and the inputs
  refers to current state before the clock edge arrives
  refers to next state after the clock edge arrives
D Flip-Flop | 
D | Q(t+1)
0 | 0 Reset
1 | 1 Set
JK Flip-Flop | 
J K | Q(t+1)
0 0 | Q(t) No change
0 1 | 0 Reset
1 0 | 1 Set
1 1 | Q'(t) Complement
T Flip-Flop | 
T | Q(t+1)
0 | Q(t) No change
1 | Q'(t) Complement

## Slide 26: Flip-Flop Characteristic Equation
The characteristic equation defines the operation of a flip-flop
For D Flip-Flop:
For JK Flip-Flop:
For T Flip-Flop:
Clearly, the D Flip-Flop is the simplest among the three
D Flip-Flop | 
D | Q(t+1)
0 | 0 Reset
1 | 1 Set
JK Flip-Flop | 
J K | Q(t+1)
0 0 | Q(t) No change
0 1 | 0 Reset
1 0 | 1 Set
1 1 | Q'(t) Complement
T Flip-Flop | 
T | Q(t+1)
0 | Q(t) No change
1 | Q'(t) Complement

## Slide 27: Timing Considerations for Flip-Flops
Setup Time (Ts): Time duration for which the data input must be valid and stable before the arrival of the clock edge.
Hold Time (Th): Time duration for which the data input must not be changed after the clock transition occurs.
Ts and Th must be ensured for the proper operation of flip-flops
Valid data-in
Data Can be Modified after Th
Clock
Rising
Edge
Th
Ts

## Slide 28: Summary
In a sequential circuit there is internal memory
  Output is a function of current inputs and present state
  The stored memory value defines the present state
  Similarly, the next state depends on current inputs and present state
Two types of sequential circuits:
  Synchronous sequential circuits are clocked (easier to implement)
  Asynchronous sequential circuits are not clocked
Two types of Memory elements: Latches and Flip-Flops
Latches are level-sensitive, flip-flops are edge-triggered
Flip-flops are better memory elements for synchronous circuits
A flip-flop is described using a characteristic table and equation