## Slide 1: Lecture # 13 Register/Shift register/Parallel load.
By: Muhammad Zain Uddin
email: zuddin@iba.edu.pk

## Slide 2: Registers
Registers
Shift Registers and their Applications

## Slide 3: Register
A register is a circuit capable of storing data
An -bit register consists of Flip-Flops and stores bits
Common clock: data is loaded in parallel at the same clock edge
Common reset: All Flip-Flops are reset in parallel
4-bit
Register

## Slide 4: Register Load (or Enable)
Question: How to control the loading of data into a register?
Solution: Introduce a register Load (or Enable) signal
If the register is enabled, load the data into the register
Otherwise, do not change the value of the register
Question: How to implement register Load?
n-bit Register

## Slide 5: Register with Parallel Load
Solution: Add a mux at the input of the register
If is 1 then If is 0 then
0
1
0
1
0
1
0
1

## Slide 6: Shift Registers
A shift register is a cascade of flip flops sharing the same clock
Allows the data to be shifted from each flip-flop to its neighbor
The output of a flip-flop is connected to the input of its neighbor
Shifting can be done in either direction
All bits are shifted simultaneously at the active edge of the clock
Serial Input SI
Serial Output SO
Right Shift Register

## Slide 7: Timing of a Shift Register
Cycle | SI | Q3 | Q2 | Q1 | Q0 = SO
T0 | 1 | 1 | 0 | 1 | 0
T1 | 0 | 1 | 1 | 0 | 1
T2 | 1 | 0 | 1 | 1 | 0
T3 | 1 | 1 | 0 | 1 | 1
T4 | 0 | 1 | 1 | 0 | 1
T5 | 1 | 0 | 1 | 1 | 0
T6 | 0 | 1 | 0 | 1 | 1
Serial Input SI
Serial Output SO

## Slide 8: Shift Register with Parallel Output
The output of a shift register can be serial or parallel
A Serial-In Parallel-Out (SIPO) shift register is shown below
All flip-flop outputs can be read in parallel
Serial Input SI
Parallel Output PO

## Slide 9: Bit Serial Adder
Adding two -bit numbers and serially over clock cycles
A bit-serial adder can be implemented using
A Full Adder
A Flip-Flop to store the carry-out
A Shift Register to store the -bit sum
Serial-In Parallel-Out
-bit Shift Register
Full
Adder
Flip
Flop
Serial Inputs
Serial Addition
Starts at the
Least-significant bit

## Slide 10: Sequence Detector with a Shift Register
A sequence detector can be implemented using:
Left Shift Register (SIPO) + AND Gates
Example: Detecting the sequences 1010 and 1100
Bits are shifted left starting at the most-significant bit
Serial Input SI
Detect
1010
Detect
1100
1
0
1
0

## Slide 11: Parallel-In Serial-Out Shift Register
A Parallel-In Serial-Out (PISO) Shift Register has:
  parallel data input lines
  Serial Input
  Serial Output
  Control input s
  Clock input
  Reset input
Two control functions:
  s = 0  Shift Data
  s = 1  Parallel Load input bits
Parallel-In Serial-Out
Shift Register
Clock
Reset
Parallel Data Input
Serial Output
Control
Serial In

## Slide 12: Parallel In Serial Out Shift Register
Two control functions:
s = 0  Shift s = 1  Load data
Serial
Output SO
1
0
1
0
1
0
Parallel Data Input
1
0
Serial
Input SI

## Slide 13: Universal Shift Register
A Universal Shift Register has the following specification:
  parallel data input and output lines
  Right-shift and Left-shift Serial Inputs
  Two control input lines s
  Clock input
  Reset input
Four control functions:
  s = 00  No change in value
  s = 01  Shift Right (Right-Shift Serial Input)
  s = 10  Shift Left (Left-Shift Serial Input)
  s = 11  Parallel Load input bits
Universal
Shift Register
Clock
Reset
2
Control
Parallel
Data
Input
L-shift
Serial
Input
R-shift
Serial
Input
Parallel Data Output

## Slide 14: Universal Shift Register Design
3
2
1
0
3
2
1
0
3
2
1
0
3
2
1
0
Parallel Inputs
Parallel Outputs
Right-Shift
Serial Input
Left-Shift
Serial Input
2
s = 0 
No change
s = 1 
Shift Right
s = 2 
Shift Left
s = 3 
Parallel Load